## Slide 1
Transmission Cryo-Electron Microscopy
A tool used by structural biologists to study
molecular nanomachines
Gabriel Lander, Thesis Defense 2009

## Slide 2
This plastic tube contains our
molecular sample of interest
Inside the tube, the nanoparticles are freely mobile.
The sample must be frozen in order to image it

## Slide 3
3mm
A tiny drop of the sample is
placed onto a copper grid

## Slide 4
3 microliters of sample
side-view of grid
A tiny drop of the sample is
placed onto a copper grid

## Slide 5
The sample is loaded into a machine called a Vitrobot
There are two blotting papers
on either side of the sample
They close on the grid and
leave a very thin layer of
molecules in solution
this chamber maintains
100% humidity and a
temperature of 4ºC

## Slide 6
Liquid Ethane
Liquid Nitrogen
The sample is then quickly plunged into liquid ethane
the sample freezes so fast that ice crystals can’t form - this is called “vitreous” ice

## Slide 7
That is how we go from sample in solution...
...to molecules frozen in thin ice

## Slide 8
Now we can reconstruct a 3D structure from the frozen molecules
The grid containing the frozen molecules is loaded into an electron microscope

## Slide 9
This is an example of a transmission
electron microscope (TEM)
FEI Tecnai F20

## Slide 10
Here are three molecules trapped in different orientations
Underneath is a detector (such as photographic film)

## Slide 11
When we shoot the molecules with an electron beam, the orientation of the particles leaves a unique “shadow”
These “shadows” contain all the 3-dimensional information of the molecule, compressed into a 2D image

## Slide 12
This is an example of an image we collect using the electron microscope
We can see the molecules as they are trapped in the ice, in different orientations

## Slide 13
Even though the image is noisy, we can see that some of the particles are trapped in the same orientation
We can select these molecules and cut them out of the image

## Slide 14
The contrast of the cut-out molecules is inverted
Although the raw data is noisy, we can rotate them so that all the molecules are in the same orientation
These “aligned” molecules are then added together
This summed image provides a more detailed view of the molecule in this orientation

## Slide 15
We perform this same process for the different orientations of the molecule
Then we gather all these views and combine them computationally

## Slide 16
Then we gather all these views and combine them computationally
This provides us with a 3D reconstruction of our molecule

## Slide 17
Zooming in, we can see structural features that tell us how the molecule functions in the cell